## Slide 1
CSC2710 – Intro to Systems and Networking
SPANNING TREE
Instructor: Susmit Shannigrahi
sshannigrahi@tntech.edu

## Slide 2
Apps (HTTP)
Transport (TCP/UDP)
Network (IP)
Link (Ethernet)
Apps (HTTP)
Transport (TCP/UDP)
Network (IP)
Link (Ethernet)
Ethernet Interface
Ethernet Interface
Segments
Data
Packets
Frames
Bits (1010001)

## Slide 3
So far...
we saw how to build a local network
How do we interconnect different types of networks to build a large global network?
Notes: Ndn can help organizing the namespaces
Once that’s done, data discovery and provenance is
Straight forward
Retrieval, transparent failover, and specialized operations
In this work, we take a real access log and try to quantify NDN’s improvements to a climate
workflow

## Slide 4
Switching
Switch
  A mechanism to interconnect
  links to form a large network
  Forward frames
  Separate the collision domains
  Filter packets between LANs
  Connects two or more LAN segments - Bridging
LAN 1
Collision domain 1
LAN 2
Collision domain 2
Notes: Ndn can help organizing the namespaces
Once that’s done, data discovery and provenance is
Straight forward
Retrieval, transparent failover, and specialized operations
In this work, we take a real access log and try to quantify NDN’s improvements to a climate
workflow

## Slide 5
Switches are self learning!
Inspect the source MAC address
  What is a mac address?
Associate mac address and incoming interface
Store this association for later use, (for some time)
  aging-timer
Notes: Ndn can help organizing the namespaces
Once that’s done, data discovery and provenance is
Straight forward
Retrieval, transparent failover, and specialized operations
In this work, we take a real access log and try to quantify NDN’s improvements to a climate
workflow

## Slide 6
Switching Table
To decide how to forward a packet, a switch consults a forwarding table
Destination, Port
-------------------------------------
A 3
B 0
C 3
D 3
E 2
F 1
G 0
H 0
Forwarding Table for Switch 2
Notes: Ndn can help organizing the namespaces
Once that’s done, data discovery and provenance is
Straight forward
Retrieval, transparent failover, and specialized operations
In this work, we take a real access log and try to quantify NDN’s improvements to a climate
workflow

## Slide 7
Switching Table
Unknown destination → send out on all Interfaces (flooding)
  Skip the incoming interface
Destination, Port
-------------------------------------
A 3
B 0
C 3
D 3
E 2
F 1
G 0
H 0
Forwarding Table for Switch 2
Notes: Ndn can help organizing the namespaces
Once that’s done, data discovery and provenance is
Straight forward
Retrieval, transparent failover, and specialized operations
In this work, we take a real access log and try to quantify NDN’s improvements to a climate
workflow

## Slide 8
Loop
Spot the loop
Why?
Notes: Ndn can help organizing the namespaces
Once that’s done, data discovery and provenance is
Straight forward
Retrieval, transparent failover, and specialized operations
In this work, we take a real access log and try to quantify NDN’s improvements to a climate
workflow

## Slide 9
Solution? Spanning Tree
Think of the extended LAN as being represented by a graph that possibly has loops (cycles)
A spanning tree is a sub-graph of this graph that covers all the vertices but contains no cycles
Spanning tree keeps all the vertices of the original graph but throws out some of the edges
Example of (a) a cyclic graph; (b) a corresponding spanning tree.
Notes: Ndn can help organizing the namespaces
Once that’s done, data discovery and provenance is
Straight forward
Retrieval, transparent failover, and specialized operations
In this work, we take a real access log and try to quantify NDN’s improvements to a climate
workflow

## Slide 10
How do we create a spanning tree?
    Properties: No loops
    How?
      Selectively flood
      Distributed algorithm, no coordination!
      Automatic reconciliation when failure occurs
Notes: Ndn can help organizing the namespaces
Once that’s done, data discovery and provenance is
Straight forward
Retrieval, transparent failover, and specialized operations
In this work, we take a real access log and try to quantify NDN’s improvements to a climate
workflow

## Slide 11
How do we create a spanning tree?
    Properties: No loops
    How?
      Selectively flood
      Distributed algorithm, no coordination!
      Automatic reconciliation when failure occurs
    Switches elect a root
      The switch with the smallest identifier
      Each switch identifies if its interface is on the shortest path from the root
      Exclude if not
    Send message (Y,d,X)
    From x, claims Y is the root, distance is d
Notes: Ndn can help organizing the namespaces
Once that’s done, data discovery and provenance is
Straight forward
Retrieval, transparent failover, and specialized operations
In this work, we take a real access log and try to quantify NDN’s improvements to a climate
workflow

## Slide 12
How do we create a spanning tree?
    Message (Y, d, X) - (to, distance, from)
    4 thinks it’s the root
    Sends (4, 0, 4) to 3 and 5
    Receives (3,0,3) from 3
      Sets it to as the root since 3 < 4
    Receives (3,1,5) from 5
      Sees that this is a longer path to 3
      2 hops vs direct path (1 hop)
      Removes 4-5 link from the tree
1
2
3
4
5
6
7
Notes: Ndn can help organizing the namespaces
Once that’s done, data discovery and provenance is
Straight forward
Retrieval, transparent failover, and specialized operations
In this work, we take a real access log and try to quantify NDN’s improvements to a climate
workflow

## Slide 13
What does 4 do when it hears from 2?
    Message (Y, d, X) - (to, distance, from)
    2 hears (1, 0, 1) from 1
    2 sends (1, 1, 2) to 3
    3 sends (1, 2, 3) to 5 and 4
    4 receives (1, 2, 3) from 3
    4 receives (1, 3, 5) from 5
    Sets 1 as root (id=1 is < id=4)
    Prunes the 4-5 path since it is 4 hops compared to 3 hops via 3
1
2
3
4
5
6
7
Notes: Ndn can help organizing the namespaces
Once that’s done, data discovery and provenance is
Straight forward
Retrieval, transparent failover, and specialized operations
In this work, we take a real access log and try to quantify NDN’s improvements to a climate
workflow

## Slide 14
Failure and Downsides
    Even after the system has stabilized, the root continues to send messages periodically
      Other bridges continue to forward these messages
    When a bridge fails, the downstream bridges will not receive the configuration messages
      After waiting a specified period of time, they will
      once again claim to be the root and the
      algorithm starts again
    No load balancing
1
2
3
4
5
6
7
Notes: Ndn can help organizing the namespaces
Once that’s done, data discovery and provenance is
Straight forward
Retrieval, transparent failover, and specialized operations
In this work, we take a real access log and try to quantify NDN’s improvements to a climate
workflow

## Slide 15
Virtual LAN (VLANs)
    LANs are on the same Ethernet segments
    Does not scale very well – too many wires
    How can we put multiple people in different locations on the same Ethernet segment (LAN)?
    How do we create multiple LANs over the same wire?
Notes: Ndn can help organizing the namespaces
Once that’s done, data discovery and provenance is
Straight forward
Retrieval, transparent failover, and specialized operations
In this work, we take a real access log and try to quantify NDN’s improvements to a climate
workflow

## Slide 16
Why separate at all?
    LANs are on the same Ethernet segments! Security.
    Isolation – sensitive traffic vs normal traffic
    Containment of traffic – your for loop broke the internet
    How do we create multiple LANs over the same wire?
Notes: Ndn can help organizing the namespaces
Once that’s done, data discovery and provenance is
Straight forward
Retrieval, transparent failover, and specialized operations
In this work, we take a real access log and try to quantify NDN’s improvements to a climate
workflow

## Slide 17
VLANs
    Switches specify which VLAN is accessible over which interface
    Each interface can have a VLAN color
    Each Mac address can have a interface color
    Add VLAN tag to the Ethernet header
Notes: Ndn can help organizing the namespaces
Once that’s done, data discovery and provenance is
Straight forward
Retrieval, transparent failover, and specialized operations
In this work, we take a real access log and try to quantify NDN’s improvements to a climate
workflow

## Slide 18
Apps (HTTP)
Transport (TCP/UDP)
Network (IP)
Link (Ethernet)
Apps (HTTP)
Transport (TCP/UDP)
Network (IP)
Link (Ethernet)
Ethernet Interface
Ethernet Interface
Segments
Data
Packets
Frames
Bits (1010001)
Link Layer Recap – All this for a cat picture